Level scheme 9Be+

---
P3/2
P1/2
F=1
S1/2
F=2

---
Transparency: Didi Leibfried

---
Transparency: Didi Leibfried

---
Scaling of ion trap quantum computers
Its easy to have thousands of coherent qubits …
but hard to control their interaction
Cirac, Zoller, Kimble, Mabuchi
Zoller, Tian, Blatt
Kielpinski, Monroe, Wineland

---
The Michigan T trap

---
© D. Leibfried
Scaling of ion trap quantum computers

---
Scaling of ion trap quantum computers

---
Scaling of ion trap quantum computers

---
„Architecture for a large-scale ion-trap quantum computer“, D. Kielpinski et al, Nature 417, 709 (2002)
Scaling of ion trap quantum computers

---
Segmented ion traps as scalable trap architecture
(ideas pioneered by D. Wineland, NIST)‏
Segmented trap electrode allow to
transport ions and to split ion strings
State of the art:
Transport of ions
Splitting of two-ion crystal
1 mm within 50 µs
tseparation ≈ 200 µs
no motional heating
small heating n ≈1
„Architecture for a large-scale ion-trap quantum computer“, D. Kielpinski et al, Nature 417, 709 (2002)
„Transport of quantum states“, M. Rowe et al, quant-ph/0205084

---
From: Blakestad et al., arXiv: 0901.0533v1 [quant-ph]

---
Single qubit gates
10-6 s
Two qubit gates (Geometric phase gates: Boulder, Innsbruck)	‏
10-5 s
10-4 s
Two qubit gates (Cirac-Zoller approach)‏
10-3 s
Single qubit coherence (magnetic field sensitive)‏
10-2 s
10-1 s
Coherence of the motion (Innsbruck)‏
100 s
Single qubit coherence (magnetic field insensitive)‏
101 s
Decoherence free subspaces
102 s
103 s
Well chosen single qubit (Boulder)‏
Realized time scales